## Slide 1: Basic Model & Load Calculation
Prepared by: Md. Yasin Arafat

## Slide 2: Shell Model

## Slide 3: Load Diagram

## Slide 4: Calculated Load Cases
Permanent Loads:
Weight of rotor components and equipment inside the nacelle, machinery, equipment, tower etc.
Hydrostatic Pressure
Ballast Pressure
Pre-tension in mooring lines
Static earth pressure
Variable Loads:
Bending moment on shear force due to turbine thrust

## Slide 5: Permanent Loads
Mass:

## Slide 6: Permanent Loads
Mass:
Name | Mass (t) | Ixx [KG. m2] | Iyy [KG. m2] | Izz [KG. m2]
Column 1 Ballast | 4898.1 | 6.98E+08 | 6.98E+08 | 9.49E+07
Column 2 Ballast | 4898.1 | 6.98E+08 | 6.98E+08 | 9.49E+07
Column 3 Ballast | 4898.1 | 6.98E+08 | 6.98E+08 | 9.49E+07
Central Column Ballast | 4514 | 6.40E+08 | 6.40E+08 | 8.08E+07
Pontoon 1 Ballst | 4225.2 | 5.28E+07 | 1.05E+09 | 1.05E+09
Pontoon 2 Ballst | 4224.9 | 1.05E+09 | 5.28E+07 | 1.05E+09
Pontoon 3 Ballst | 4224.9 | 1.05E+09 | 5.28E+07 | 1.05E+09
Tower | 1574 |  |  | 

## Slide 7: Permanent Loads
Pre tension In mooring line:
Line breaking strength MN 103.8
Its weight alone is approximately 26.14 MN.
Load on fairlead can’t exceed 103.8 MN
Static Earth pressure:
Not Applicable I Think

## Slide 8: Variable Loads
Tower Base moment and shear force
Formula for moment, M= Thrust x Tower Height
Formula for shear force, Fs= -Thrust
Both formulas are verified by Ansys prob tool.
Result:
Next Page

## Slide 9: Variable Loads
Result:
Wind Speed (m/s) | Pitch (deg) | Rotor Speed (rpm) | Thrust (KN) | Moment (KN.M) | Shear Force KN
3 | 0.58064 | 1.84662 | 464 | 71920 | -464
4 | 0.33798 | 2.46216 | 622 | 96410 | -622
5 | 0.00915 | 3.0777 | 812 | 125860 | -812
6 | -0.33797 | 3.69324 | 1158 | 179490 | -1158
7 | -0.63879 | 4.30878 | 1557 | 241335 | -1557
8 | -0.97996 | 4.92432 | 2011 | 311705 | -2011
9 | -1.3268 | 5.53986 | 2482 | 384710 | -2482
10 | 0.73192 | 6.1554 | 2658 | 411990 | -2658
11 | 2.42859 | 6.77094 | 2768 | 429040 | -2768
12 | 5.09471 | 7.0611 | 2478 | 384090 | -2478
13 | 7.26585 | 7.0611 | 2209 | 342395 | -2209
14 | 9.01413 | 7.0611 | 2008 | 311240 | -2008
15 | 10.53731 | 7.0611 | 1859 | 288145 | -1859
16 | 11.91818 | 7.0611 | 1733 | 268615 | -1733
17 | 13.20451 | 7.0611 | 1658 | 256990 | -1658
18 | 14.42148 | 7.0611 | 1543 | 239165 | -1543
19 | 15.58471 | 7.0611 | 1451 | 224905 | -1451
20 | 16.70423 | 7.0611 | 1382 | 214210 | -1382
21 | 17.7886 | 7.0611 | 1322 | 204910 | -1322
22 | 18.84311 | 7.0611 | 1268 | 196540 | -1268
23 | 19.87209 | 7.0611 | 1222 | 189410 | -1222
24 | 20.87848 | 7.0611 | 1178 | 182590 | -1178
25 | 21.86473 | 7.0611 | 1152 | 178560 | -1152

## Slide 10: Stress At Tower Base Moment

## Slide 11: Stress At Hydrostatic Pressure

## Slide 12: Stress At Ballast Pressure Pressure

## Slide 13: Stress At Ballast Pressure Pressure

## Slide 14: Stress All Load Combined